## Slide 1
● Centre of Gravity Track
● Zero Lift Axis
● When to use each one ?
● The “Box”
● Warm-Up manoeuvres
● Wing Rocks
● Steep / Shallow, Neg & Pos
● Basics Rules of Judging
● Turns
● Slow Rolls
● Flick Rolls
● Spins
● Loops and Eights
● Stall Turns
● Humpty Bumps
● Tail Slides
● Rolling Circles
● Positioning mark
● Handling the major errors
A Quick Zoom through the Rules

## Slide 2
The Centre of Gravity Track is the imaginary line that the aircraft centre of gravity draws as it flies along.
Imagine the aeroplane condensed into a dot, and watch the path that the dot takes through the sky. This is the Flight Path, or Track of the aeroplanes' Centre of Gravity.
To judge the flight path, compare the CGT against the horizon or the box 'A' or 'B' axes.
Example 1
The aeroplane is required to transit from a vertical down-line to horizontal flight. Although the ZLA remains horizontal after the 90° corner has been completed, the CGT will in reality continue to descend a little below the required horizontal line.
Example 2
Here the transit is from a vertical up-line to normal horizontal flight. The CGT must remain in a level horizontal line, whilst the aircraft speed will increase from very slow and the angle of attack reduces accordingly.
CGT and Angle of Attack
Judges must always look at the CGT and not be "fooled" by a high angle of attack at low speed – this can be particularly noticeable when the aeroplane is inverted, as with most aircraft the nose will appear un-naturally high.
Centre of Gravity Track (CGT)

## Slide 3
Zero Lift Axis (ZLA)
The "Zero Lift Axis" of an aircraft is purely a function of its shape and aerodynamic qualities.
When flying a true vertical line in still air, the ZLA will be exactly perpendicular to the ground.
In the left and centre sketches the aeroplane is flying vertically downwards with its ZLA through the main axis.
The sketch on the far right shows that the CGT can be different to the ZLA because of the wind.
On all 45° and vertical lines we use the ZLA to tell us how accurately the aircraft is flying the figure.
Note again that in level CGT flight the wing must have a positive or negative Angle of Attack relative to the airflow, to keep the aircraft flying.

## Slide 4
When should we use CGT
and when should we use ZLA?
In horizontal lines or curving, rotating or rolling manoeuvres – use CENTRE OF GRAVITY TRACK (CGT)
When we are judging vertical or 45° lines up or down – use the ZERO LIFT AXIS (ZLA)

## Slide 5
Steep or Shallow …. Negative or Positive

## Slide 6
The “box” is the 1,000m cube of airspace within which all competition aerobatic flights are executed.
The ‘main’ box centre-line is called the “A” axis
The box ‘cross’ centre-line is called the “B” axis
Judges sit between 100 and 250m from the box edge
The ‘official’ or ‘contest wind’ will be either from the left or the right, on the “A” axis
Figures must be flown in the correct direction on the “A” axis
Figures can be flown either toward or away from the judges on the “B” axis
The Aerobatic Performance Zone
The minimum Operating Height (the low line)
depends on the Category:
The ‘Official Wind’ defines the main box axis
100m - power Unlimited
200m - power Advanced + Intermediate - glider Unlimited + Advanced
300m - power Sports + Intermediate - glider Sports + Intermediate
450m - power and glider Club
CIVA
National
e.g. GBR

## Slide 7
Warm-Up Manoeuvres / Figures
In power Intermediate / Y52, Advanced and Unlimited categories –
Any number of Half-Rolls PLUS any of the following …
Push-Pull stick inputs to check seat-belt tightness
Any number of erect or inverted 90° to 360° Turns without rolls
Stall Turns without rotations Upward Humpty Bumps without rotations Either of these two horizontal eights
PLUS up to three of -
Stall Turns 5.2.1 … 1 to 4
Humpty Bumps 8.4 rows 1 to 4 columns 1 and 2
Horizontal 8’s
7.8.4.1 and 7.8.1.1
Revised for 2022
It is recommended that competitors carry-out some Warm-Up exercises before starting the sequence, to check the aeroplane and acclimatise to +/- G forces

## Slide 8
Wing Rocks
For Power
BEFORE the sequence starts:
● There should be THREE consecutive Wing Rocks
● They can start and/or finish inside or outside the box
● Each one should reach at least 45° of roll
● They must be done along the initial sequence axis
● Climbing or diving at up to 90° is allowed
● From a 90° climb an erect or inverted exit is OK
● If not climbing at 90° then for an inverted start all wing rocks must be completed while inverted
To signify an Interruption or Break:
We need to see THREE Wing Rocks
To restart after a Break:
It’s the SAME process as the very start
If there was no prior direction error then the pre-break direction MUST be resumed
If there was a direction error immediately before the break then the restart direction can be different to that before the break

## Slide 9
The Basic Rules of Judging
Radii 'A' and 'E' need not be the same, but 'E' is flown much more slowly.
Lines 'B' and 'D' must be the same length.
For a 2/1 ratio : deduct 2 marks
For a 3/1 ratio : deduct 3 marks
No line at all : deduct 4 marks
For example:
If the aircraft starts the figure climbing at 5°, no yaw and between 5° and 10° of bank
During the figure is pitched OK but yawed 5° and rolled 10° off axis at a key point
The figure ends with 5° of yaw, between 0° and 5° nose-down and no bank angle
Every figure starts with a potential 'perfect' mark or grade of 10 points
The basic judging rule is : an error of 5° equals a 1 point downgrade
Deduct points to arrive at your personal final mark for each figure
The result is: 10 points - 1 - 0 - 1.5 ... - 0 - 1 - 2 ... - 1 - 0.5 - 0 = 3 marks for the figure
This is a fault driven process - you are not marking "goodness".

## Slide 10
Turns
Types:
Turns can be either erect or inverted
Amounts are 90°, 180°, 270° and 360°
Actions:
Roll to at least 60° of bank For gliders this is exactly 60°
Turn at a constant rate through the required angle
Maintain the turn rate and altitude
Stop exactly on heading, and then
Roll back to wings-level
Not judged:
The shape of the turn, there is no correction for the effect of wind
The size of the turn
This is NOT a ‘PPL’ turn – think more of a “jerky marionette”

## Slide 11
Slow Rolls
Many variations of slow rolls are used in a great variety of figures, often preceded and followed by lines which must be judged for CGT (where horizontal) or ZLA (where at 45° or in the vertical) and also for comparative length.
Slow rolls, many of which include hesitations, are sometimes called aileron rolls to distinguish them from flick or snap rolls.
In a slow roll the rotation is primarily driven by aileron action, whereas a flick roll combines yaw and pitch inputs to cause 'auto-rotation'.

## Slide 12
Flick or Snap Rolls
Flick-rolls happen so quickly it is your subjective 'perception' as to whether the pitch and yaw have –
caused auto-rotation
stayed there during the roll
been removed to stop it
If you are not convinced then you should award a Perception Zero (PZ) instead of a normal mark
Flick rolls are initiated by rapid pitch and yaw control inputs, causing one wing to stall whilst the other continues to fly - leading to very high acceleration in roll This abrupt high energy translation makes the manoeuvre hard to study and hence difficult to judge accurately

## Slide 13
Spins
If you are not convinced that there was a genuine stall then you should award a Perception Zero (PZ) instead of a normal mark
The ‘competition’ spin must display these characteristics –
A clean initial stall in level on-axis CGT flight, leading to
Immediate nose drop + wing drop + and yaw into auto-rotation
The rotation must stop on the correct heading
We must see rapid translation to a vertical ZLA line
If there is a linked roll then it must be treated as a hesitation, i.e. with a minimum pause
A smooth radius pull or push, to … (level flight exit, remainder of figure etc.)

## Slide 14
Loops and Eights
A partial or complete loop takes place when the aeroplane pitches through at least 45° without roll or yaw, either in positive (pull) or negative (push) flight.
Looping segments are always judged on flight path or CGT - never ZLA.
Loops, eights and vertical 'S's are always wind corrected, their elements must be accurate and 'round'.
In a simple loop (see right) the end point should be exactly where the loop started, both horizontally and vertically.
Hold up your finger, a pencil or pen to keep track of this important position.
Unless you have an easy-to-apply method they can be quite difficult to judge

## Slide 15
Judging loop shapes
The exit point should be at exactly the same level as the entry point.
The four quadrant radii and centre points are all exactly the same.
The centre-top point is exactly above the start point.
Wherever you see these 3 'truths' you can be sure that the loop is round.

## Slide 16
Half-loops with Rolls
When a half-loop upwards or downwards has some rolling at the start or end of the looping segment, there must be NO horizontal line between the rolls and the looping arc.
Memorise the size of looping arcs as they are being flown:
Where no line is drawn there is no downgrade to apply.
If you see any line at all then at least a one point downgrade must be applied.
As the length of this unwanted line increases but remains less than the half-loop radius, two to three points should be deducted.
If the length of the line exceeds the half-loop radius you must award a PZ (Perception Zero) for the figure.

## Slide 17
Stall Turns
The Stall Turn or Hammerhead is one of the most graceful aerobatic figures.
The figure can be divided into a series of sections for judging:
Smooth radius CGT entry and pull / push to the vertical.
The ZLA vertical up-line, and assessment of any rolls super-imposed.
The turn itself, which must be purely yaw with no rolling or pitching.
The ZLA down-line, and assessment of any rolls super-imposed.
The smooth radius pull / push and exit to level CGT flight.
Stall Turns with 45° entry and/or exit segments may also have rolls super-imposed there.

## Slide 18
Humpty Bumps
The ‘Humpty’ can be vertical or at 45°, it can start by going up or going down, and there is even a ‘double’ version with one vertical up and one vertical down.
All types are basically similar – they comprise looping segments that connect lines upon which a great variety of rolls can be placed.
Smooth CGT radius entry and pull / push to reach the first line.
The first ZLA line, and assessment of any rolls super-imposed.
A smooth radius half-loop.
The second ZLA line, and assessment of any rolls super-imposed.
The smooth radius pull / push and exit to level CGT flight.
All partial loop segments may have different radii, therefore in a double-humpty the two half-loops can be of different sizes.

## Slide 19
Tail Slides
Tail Slides have very similar judging criteria to Stall Turns, but there are no 45° entry and exit options – they are all vertical, and of course they start upwards.
Break the figure into the following parts for judging:
A smooth CGT radius entry and pull / push to reach the vertical up-line.
The first ZLA line, and assessment of any rolls that must be central in the line.
The slide must be either canopy-up or canopy-down, or you can think of it as wheels-down or wheels-up.
The vertical ZLA attitude must be maintained to the top and in the slide.
After the pendulum is finished, assess the second ZLA line, and any rolls again must be central in the line.
A smooth radius pull / push and exit to level CGT flight.

## Slide 20
Rolling Turns – page 1
All versions of “Rollers” combine turns with continuous rolling, and they all follow the same set of rules and judging criteria.
Break the figure into the following parts for judging:
Start in level CGT flight precisely on-heading.
There must be a constant –
  rate of turn round the circle
  rate of roll at all times
  no climbing or diving
At every Intermediate Point (with the wings level or vertical) the turn angle must be correct
The exit point must be reached on-axis with all rolling exactly completed
Rolling Turns can include whole or half rolls, or a combinations of both. The rolls can be inwards (inner wing going down) or outwards (inner wing going up) or both types alternated for the In / Out versions with a short pause between.

## Slide 21
Rolling Turns – page 2
In reality you will see many Rolling Turns flown as a series of “pull” and “push” arcs with straighter segments between them, giving a rather jerky appearance.
Here is a 90° TURN with 360° of ROLL – Aresti 2.1.3.1
Watch the START very carefully:
You must see Rolling and Turning begin together
When the Roll reaches 45° the Turn is already 12.5°
At the 1st wings vertical Intermediate Point the turn angle reached must be 22.5° (1/4 of 90°)
At the inverted Intermediate Point the Turn is 45° and the figure is exactly HALF completed
Often the pilot will “Pull” through 60-70° (first half) and “Push” through only 20-30° (second half)
The Roll and Turn must both finish at the 90° point
The CGT or flight path must finish ON AXIS.
This figure CAN be flown very convincingly but it does need well co-ordinated rudder and stick inputs. Just watch every part carefully and make a running total of the errors.

## Slide 22
The Positioning Mark
Use the CIVA system to identify figures that are not placed in an optimum position to be judged, within the context of the sequence.
Where a figure is –
Too far to the left = “L”
Much too far left = “LL”
Too far to the right = “R”
Much too far right = “RR”
Too near = “N”
Much too near = “NN”
Too far = “F”
Much too far = “FF”
so a figure could be “L” or “NLL” or “FFR” or even “NNRR” etc.
After the flight –
Total the number of letters
Count each one as a half mark (e.g. “N” and “FR” and “LL” and “NL” gives 3.5 downgrades)
Deduct this total from ten and therefore: 10.0 – 3.5 = 6.5 as the Position Mark)
This is your “starter” Positioning Mark, which you can ‘adjust’ up / down by 1 mark if necessary.

## Slide 23
Handling the Major Errors
A figure that receives ten or more downgrades must be awarded a Numeric Zero = 0.0
When cumulative errors in roll / pitch / yaw total more than 45° but less than 90° you should award a Numeric Zero = 0.0
Subjective
personal
Judgement: No Video
Critical errors of Perception (e.g. in Flick Rolls) should be awarded a Perception Zero = PZ
Where a Major Error is seen: an element is flown in the wrong direction, part of the figure is different to the Aresti symbols on the Judging Form, the wrong hesitations in a Roll are seen, or there is more than 90° of cumulative error seen …. the figure must be awarded a Hard Zero = HZ
Clear
matters of
Fact: Video

## Slide 24: Your questions please … !